## Slide 1
copyright by the 3MF Consortium 2019
3MF Technical Working Group
Volumetric extension specification
2019/06/26
New York

## Slide 2: Volumetric extension - Overall concept
Enrich geometry of 3MF with volumetric elements that can represent spatially varying properties
Inefficient to handle with a mesh representation, especially in cases where the variation is continuous in space. => Use a 3D Texture-based or field-based representation. => Encode complex objects by explicitly specifying their properties at any point in space

## Slide 3
Which information should we encode
Volumetric extension
Encodes complex objects by specifying their properties at any point in space
1. Object boundary (Levelset) a single scalar value at each point in space. - If value > threshold => material - If value <= threshold, void

## Slide 4
Volumetric extension
Encodes complex objects by specifying their properties at any point in space
Object boundary (Levelset)
Spatially varying Color Three scalar values (R, G, B) between 0 and 1 at each point in space
Which information should we encode
Channel R
Channel B
Channel G

## Slide 5
Which information should we encode
Intensity “Material 1”
Intensity “Material 2”
Volumetric extension
Encodes complex objects by specifying their properties at any point in space
Object boundary (Levelset)
Spatially varying Color
Material composition: - Multiple scalar channels with intensities between [0,1] - Each associated with a basematerial - Mixing according to their intensity

## Slide 6
Volumetric extension
Encodes complex objects by specifying their properties at any point in space
1 -3 …
High level (arbitrary) properties: - Single channel with scalar intensity/value - Encode intensity of an abstract property: (“conductivity”, “density”, “elasticity”, …) - Consumer can decide, how they mix materials to achieve that property
Which information should we encode

## Slide 7
Building blocks
1. Scalar function that assigns every point in space a scalar value
Image3D: A list of PNGs with RGBA, RGB, Grey, GreyAlpha - values
Image3DChannelSelector
  Picks a channel
  Defines min max range
  Defines interpolation
  Defines repetition in space

## Slide 8
Building blocks
2. Combination rules for those functions
Boolean operations/mixing/masking: h(x,y,z) = a*f(x,y,z) + b*g(x,y,z) h(x,y,z) = f(x,y,z) * g(x,y,z) h(x,y,z) = m(x,y,z)*f(x,y,z) + (1-m(x,y,z))*g(x,y,z)
a
b
h, g, f
m
+,*, mask

## Slide 9
2. Combination rules for those functions
Boolean operations/mixing/masking: h(x,y,z) = a*f(x,y,z) + b*g(x,y,z) h(x,y,z) = f(x,y,z) * g(x,y,z) h(x,y,z) = m(x,y,z)*f(x,y,z) + (1-m(x,y,z))*g(x,y,z)
a
b
+,*
h, g, f
blendmthod=“mix” and “multiply”

## Slide 10
2. Combination rules for those functions
Boolean operations/mixing/masking: h(x,y,z) = a*f(x,y,z) + b*g(x,y,z) h(x,y,z) = f(x,y,z) * g(x,y,z) h(x,y,z) = m(x,y,z)*f(x,y,z) + (1-m(x,y,z))*g(x,y,z)
mask
h, g, f
m
blendmthod=“mask”

## Slide 11
Building blocks
2. Combination rules for those functions
2. transforming them (affine linear):
g(x,y,z) = f(A(x,y,z) + b)
f
A, b

## Slide 12
Building blocks
3. Evaluate manipulated functions in 3MF world
Object boundary (Levelset)
Spatially varying Color
Material composition
High level (arbitrary) properties
Channel “Mat 1”
Channel “Mat 2”

## Slide 13
Examples
Shared resources

## Slide 14
Examples
3. Evaluate manipulated functions in 3MF world
Object boundary (Levelset)

## Slide 15
Examples
3. Evaluate manipulated functions in 3MF world
Spatially varying color

## Slide 16
Channel “mat1”
Channel “mat2”
Examples
3. Evaluate manipulated functions in 3MF world
Material composition:

## Slide 17
Building blocks
3. Evaluate manipulated functions in 3MF world
High level (arbitrary) properties:

## Slide 18
Questions/Issues?
…