## Slide 1
copyright by the 3MF Consortium 2019
3MF Technical Working Group
Volumetric extension specification
2019/03/06
Tel Aviv

## Slide 2: Volumetric extension - Overall concept
Enrich geometry of 3MF with volumetric elements that can represent spatially varying properties
Inefficient to handle with a mesh representation, especially in cases where the variation is continuous in space. => Use a 3D Texture-based or field-based representation. => Encode complex objects by explicitly specifying their properties at any point in space

## Slide 3
Which information should we encode
Volumetric extension
Encodes complex objects by specifying their properties at any point in space
1. Object boundary (Levelset) a single scalar value at each point in space. - If value > threshold => material - If value <= threshold, void

## Slide 4
Volumetric extension
Encodes complex objects by specifying their properties at any point in space
Object boundary (Levelset)
Spatially varying Color Three scalar values (R, G, B) between 0 and 1 at each point in space
Which information should we encode
Channel R
Channel B
Channel G

## Slide 5
Which information should we encode
Channel 1
Channel 2
Volumetric extension
Encodes complex objects by specifying their properties at any point in space
Object boundary (Levelset)
Spatially varying Color
Material composition: - Multiple scalar channels with intensities between [0,1] - Each associated with a basematerial - Mixing according to their intensity

## Slide 6
Volumetric extension
Encodes complex objects by specifying their properties at any point in space
1 -3 …
High level (arbitrary) properties: - Single channel with scalar intensity/value - Encode intensity of an abstract property: (“conductivity”, “density”, “elasticity”, …) - Consumer can decide, how they mix materials to achieve that property
Which information should we encode

## Slide 7
Building blocks
1. Scalar function that assigns every point in space a scalar value
Image3D: A list of PNGs with RGBA, RGB, Grey, GreyAlpha - values
Image3DChannelSelector
  Picks a channel
  Defines min max range
  Defines interpolation
  Defines repetition in space

## Slide 8
Building blocks
2. Combination rules for those functions
Boolean operations/mixing/masking: h(x,y,z) = a*f(x,y,z) + b*g(x,y,z) h(x,y,z) = f(x,y,z) * g(x,y,z) h(x,y,z) = m(x,y,z)*f(x,y,z) + (1-m(x,y,z))*g(x,y,z)
a
b
*, +
h, g, f

## Slide 9
Building blocks
2. Combination rules for those functions
2. transforming them (affine linear):
g(x,y,z) = f(A(x,y,z) + b)
g, f
A, b

## Slide 10
Building blocks
3. Evaluate manipulated functions in 3MF world
Object boundary (Levelset)
Spatially varying Color
Material composition
High level (arbitrary) properties
Channel 1
Channel 2

## Slide 11
Building blocks
3. Evaluate manipulated functions in 3MF world
Object boundary (Levelset)

## Slide 12
Building blocks
3. Evaluate manipulated functions in 3MF world
Spatially varying color

## Slide 13
Channel 1
Channel 2
Building blocks
3. Evaluate manipulated functions in 3MF world
Material composition:

## Slide 14
Building blocks
3. Evaluate manipulated functions in 3MF world
High level (arbitrary) properties: