## Slide 1
copyright by the 3MF Consortium 2018
3MF Technical Working Group
Volumetric specification
28th/29th November 2018
Boston, MA
401 Edgewater Place
Suite 600
Wakefield, 01880 MA
USA

## Slide 2
copyright by the 3MF Consortium 2018
Encode geometric information in volumes
Volumetric extension
Encodes complex objects by specifying their properties at any point in space

## Slide 3
copyright by the 3MF Consortium 2018
Which information should we encode
Volumetric extension
Encodes complex objects by specifying their properties at any point in space
Object boundary (Levelset)

## Slide 4
copyright by the 3MF Consortium 2018
Volumetric extension
Encodes complex objects by specifying their properties at any point in space
Object boundary (Levelset)
Discrete properties:
Discrete basematerial per location
Which information should we encode

## Slide 5
copyright by the 3MF Consortium 2018
Volumetric extension
Encodes complex objects by specifying their properties at any point in space
…
High level properties: - Multiple scalar channels with intensities between [0,1] - Encode intensity of an abstract property: (“conductivity”, “density”, “elasticity”, “color rgb R”…) - Consumer can decide, how they mix materials to achieve that
OR
Composites:
Multiple scalar channels with intensities between [0,1]
Each associated with a basematerial
Mixing according to their intensity
Which information should we encode
Channel 1
Channel 2

## Slide 6
copyright by the 3MF Consortium 2018
Building blocks
1. Scalar function that assigns every point in space a scalar value
Image3D: A list of PNGs with RGBA, RGB, Gray, GrayAlpha - values
Image3DChannelSelector
  Picks a channel
  Defines min max range
  Defines interpolation
  Defines repetition in space

## Slide 7
copyright by the 3MF Consortium 2018
Building blocks
2. Combination rules for those functions
Boolean operations: h(x,y,z) = a*f(x,y,z) + b*g(x,y,z) h(x,y,z) = f(x,y,z) * g(x,y,z)

## Slide 8
copyright by the 3MF Consortium 2018
Building blocks
2. Combination rules for those functions
2. transforming them (affine linear):
g(x,y,z) = f(A(x,y,z) + b)

## Slide 9
copyright by the 3MF Consortium 2018
Building blocks
2. Combination rules for those functions
Reevaluating them (UVW mapping):
g(x,y,z) = f(u(x,y,z), v(x,y,z), w(x,y,z))

## Slide 10
copyright by the 3MF Consortium 2018
Building blocks
3. Evaluate manipulated functions in 3MF world
To encode Object boundaries

## Slide 11
copyright by the 3MF Consortium 2018
Building blocks
3. Evaluate manipulated functions in 3MF world
To encode materials

## Slide 12
copyright by the 3MF Consortium 2018
Building blocks
3. Evaluate manipulated functions in 3MF world
To encode mixing: TODO