## Slide 1
copyright by the 3MF Consortium 2018
3MF Technical Working Group
Volumetric specification
Original: 28th/29th November 2018
Updated: 20th December 2018
Boston, MA
401 Edgewater Place
Suite 600
Wakefield, 01880 MA
USA

## Slide 2
copyright by the 3MF Consortium 2018
Encode geometric information in volumes
Volumetric extension
Encodes complex objects by specifying their properties at any point in space

## Slide 3
copyright by the 3MF Consortium 2018
Which information should we encode
Volumetric extension
Encodes complex objects by specifying their properties at any point in space
1. Object boundary (Levelset)

## Slide 4
copyright by the 3MF Consortium 2018
Volumetric extension
Encodes complex objects by specifying their properties at any point in space
Object boundary (Levelset)
Discrete material properties:
Discrete basematerial per location
Which information should we encode
Removed

## Slide 5
copyright by the 3MF Consortium 2018
Volumetric extension
Encodes complex objects by specifying their properties at any point in space
Object boundary (Levelset)
Spatially varying Color
Which information should we encode

## Slide 6
copyright by the 3MF Consortium 2018
Which information should we encode
Channel 1
Channel 2
Volumetric extension
Encodes complex objects by specifying their properties at any point in space
Object boundary (Levelset)
Spatially varying Color
Material composition: - Multiple scalar channels with intensities between [0,1] - Each associated with a basematerial - Mixing according to their intensity

## Slide 7
copyright by the 3MF Consortium 2018
Volumetric extension
Encodes complex objects by specifying their properties at any point in space
1 -3 …
High level (arbitrary) properties: - Single channel with scalar intensity/value - Encode intensity of an abstract property: (“conductivity”, “density”, “elasticity”, …) - Consumer can decide, how they mix materials to achieve that property
Which information should we encode

## Slide 8
copyright by the 3MF Consortium 2018
Building blocks
1. Scalar function that assigns every point in space a scalar value
Image3D: A list of PNGs with RGBA, RGB, Gray, GrayAlpha - values
Image3DChannelSelector
  Picks a channel
  Defines min max range
  Defines interpolation
  Defines repetition in space

## Slide 9
copyright by the 3MF Consortium 2018
Building blocks
2. Combination rules for those functions
Boolean operations/mixing: h(x,y,z) = a*f(x,y,z) + b*g(x,y,z) h(x,y,z) = f(x,y,z) * g(x,y,z)

## Slide 10
copyright by the 3MF Consortium 2018
Building blocks
2. Combination rules for those functions
2. transforming them (affine linear):
g(x,y,z) = f(A(x,y,z) + b)

## Slide 11
copyright by the 3MF Consortium 2018
Building blocks
2. Combination rules for those functions
Reevaluating them (UVW mapping):
g(x,y,z) = f(u(x,y,z), v(x,y,z), w(x,y,z))
Removed

## Slide 12
copyright by the 3MF Consortium 2018
Building blocks
3. Evaluate manipulated functions in 3MF world
To encode Object boundaries
Reformulated

## Slide 13
copyright by the 3MF Consortium 2018
Building blocks
3. Evaluate manipulated functions in 3MF world
To encode materials
Reformulated

## Slide 14
copyright by the 3MF Consortium 2018
Building blocks
3. Evaluate manipulated functions in 3MF world
Object boundary (Levelset)

## Slide 15
copyright by the 3MF Consortium 2018
Building blocks
3. Evaluate manipulated functions in 3MF world
Spatially varying color

## Slide 16
Channel 1
Channel 2
copyright by the 3MF Consortium 2018
Building blocks
3. Evaluate manipulated functions in 3MF world
Material composition:

## Slide 17
copyright by the 3MF Consortium 2018
Building blocks
3. Evaluate manipulated functions in 3MF world
High level (arbitrary) properties: