## Slide 1: ReDefining A in RGBA: Towards a Standard for Graphical 3D Printing
Philipp Urban
Competence Center for 3D Printing Technology
Fraunhofer Institute for Computer Graphics Research (IGD)

## Slide 2: Application areas
Replacements parts fitting into existing visual environment
Source: zahnaufhellung-friedrichshafen.de
Design prototypes
Source: Audi
Cultural heritage
Source: bbc.com
Entertainment

## Slide 3
Redefining A in RGBA: Towards a Standard for Graphical 3D Printing
Philipp Urban, Tejas Madan Tanksale, Alan Brunton, Bui Minh Vu, Shigeki Nakauchi ACM Transactions on Graphics, Volume 38, Issue 3, Article 21, May 2019
Preprint on arXiv incl. Matlab scripts: https://arxiv.org/abs/1710.00546

## Slide 4
International Color Consortium (ICC)

## Slide 5
ICC established a standard for color management that is used worldwide by software and hardware companies
It is also an ISO standard: ISO 15076-1:2010
Open System Architeture

## Slide 6
iccMAX
New standard called “iccMAX” introduced covering visual material properties beyond color, i.e. managing BRDFs, spectral, etc. information
ISO 20677
Open source reference implementation available
Is not linked to a specific file format, i.e. it can also be used together with OBJ, WRL and 3MF

## Slide 7
Discussion with ICC’s Technical Secretary, Phil Green:
Define a specific iccMAX-“Interoperability Conformance Specification” (ICS) for RGBA (fill out the ICS form)
Register the ICS (it has to be approved by the ICC)
RGBA
(ICS)
iccMAX

## Slide 8
File Format Requirements for Appearance 3D Printing

## Slide 9
General requirements:
File format has to store optical material properties / visual attributes (percepts for color, gloss, translucency, anisotropic color) in addition to 3D shape
Device independent
Optical material properties / visual attributes must be measureable
Low dimensional
A conversion into a perceptually-uniform space is desired (for process control, quality assurance, gamut mapping)
Practical/political constraints:
Defining an independent file format will not be accepted in industry  extension of an existing format
Small extensions  easier inclusion into format
Extensions in-line with other formats (e.g. measurement cond.)  easier inclusion into format
Data can already be encoded in existing file format (e.g. RGBA)  easier inclusion into format
color
Translucency
Gloss
File Format Requirements for Appearance 3D Printing
anisotropic
color

## Slide 10
RGBA textured 3D models are
supported by various 3D file formats
can be created and modified by various 3D modeling tools
RGBA textures can be modified by image processing tools
RGBA is low dimensional
Advantages to use RGBA for Color + Translucency Encoding

## Slide 11
How to ensure device independence?
How to measure RGBA for real materials?
What about perceptual-uniformity? (for process control, quality assurance, gamut mapping)
Open Questions in using RGBA for 3D printing

## Slide 12
Problem with A in RGBA as a Blending Parameter
A is used as a blending parameter to produce transparent overlays in image composition assuming additive color mixture  physically wrong, just color
Does not describe lateral scattering (LS)  Texture or geometry blurring cannot be described
Is neither linked to any measurable physical nor perceptual quantity
(1,0,0)
(0,0,1)
(0.5,0,0.5)
Source :https://dqlin.xyz/tech/2016/12/02/03_sss/
Not considering LS
considering LS

## Slide 13
Current 3MF “A in RGBA” definition
Is defined for materials, i.e. viewing conditions, measurement conditions, transformation to a perceptually uniform color space
Is undefined for materials
In materials and properties extension: additive blending

## Slide 14
Circular 45/0 measurement geometry for object colors defined
sRGB
CIE 1931 Standard Observer
Transform into the nearly perceptually-uniform CIELAB color space exist
Measureable (ICC)
Defined Viewing Conditions
Linked to a perceptually-uniform color space

## Slide 15
Light Transport and Translucency Perception

## Slide 16
Optical Material Properties (intrinsic)
Radiative Transfer Equation:
Refraction
  refractive index 
Scattering
  phase function
  scattering coefficient
Absorption
  absorption coefficient
air material
photon
Mean free path

## Slide 17
Optical Material Properties (phenomenological)
Material
Irradiance
Radiance
BSSRDF
Bidirectional Surface Scattering Reflectance Distribution Function (BSSRDF)

## Slide 18
Perceptual Attributes
Color
Texture
Gloss
Translucency
Stimulus
Viewing Conditions
Material
Human Visual System

## Slide 19
Reproducing Physical Quantities?
Material
Can we reproduce given BSSRDFs?
Mostly impossible due to printing systems limits:
Absorption (coefficients)
Scattering (coefficients / function)
Refractive index
Resolution (surface roughness)
Why not using BSSRDFs?
High dimensionality
  High memory consumption
Measurement effort
  Instruments not available
  Time consuming
No perceptual metric

## Slide 20
Perceptual Attributes
Perceived Translucency
Specular
Specular removed
Decreasing Luminance Contrast
Increasing (Inverse) Lum. Contrast
“Physics of translucency is simply too complex for the [human] visual system to run the generative equations “in reverse” and estimate intrinsic physical parameters via inverse optics.
… instead the visual system relies on simple image heuristics [cues] that correlate with translucency.”
Fleming and Bülthoff, 2005
Motoyoshi, 2010

## Slide 21
Visual cues induced by light transport
Material
Vertical
Transparent
Opaque
Lateral Light Transport
Vertical Light Transport
Lateral
PSF
Material

## Slide 22
Defining A in RGBA

## Slide 23
Redefining A in RGBA
Basis Radiative Transfer Equation:
varying (const for )
isotropic
varying (const for )
Where
is a set of virtual reference materials
is defined by wavelength independent absorption and scattering coefficients
is a modified attenuation coefficient
is a psychometric function
is dependent on and determined by
For any material , , even if

## Slide 24
Linking A, reference materials, measurements, and visual cues
To connect to the real world, we need to decide on a measurement setup.
Given the measurement setup, we first simulate measurements of the reference materials.
We obtain virtual measurements corresponding to our visual cues.

## Slide 25
Linking A, reference materials, measurements, and visual cues
Now we can apply our measurement setup to real materials.
We obtain the same measurement quantities.
Look up the best-matching reference material.
Compute 𝐴.

## Slide 26
Measuring Lateral and Vertical Light Transport
Lateral light transport
Vertical light transport
Barbieri Spectro LFP: Commercial reflection/transmission spectrophotometer Reflectance 45/0, Transmittance d/0

## Slide 27
Measuring Lateral and Vertical Light Transport
Simulations of measurements for reference materials
CAD design of the Barbieri Spectro LFP optical path
Defined sample size (must be used also for real samples later)
Solving the spectral radiative transfer equation for the reference materials and the viewing conditions
We used the physically-based path-tracer Mitsuba
Based on these measurements the Lookup table is created
CAD Design for the measurement head
We work with Barbieri on a reflectance/transmittance spectrophotometer for automatically measuring RGBA

## Slide 28
Examples
Original
Wavelength dependent absorption coefficient
Scattering coefficient 4 cm-1
Phase function: Henyey-Greenstein 0.7 (forward scattering)
Reference Material
Closest reference material
Color Adjusted Ref. Mat.
Copy a*,b* pixel values from original
Copy median lightness from original

## Slide 29
Examples
Original
Scat coeff. 12 cm-1
Phase function: Henyey-Greenstein -0.7 (backward scattering)
Reference Material
Closest reference material
Original
Scat coeff. 12 cm-1
Phase function: Henyey-Greenstein -0.7 (backward scattering)
Color Adjusted Reference Materials
Copy a*,b* pixel values from original
Copy median lightness from original

## Slide 30
Perceptually-Uniform Embedding of A

## Slide 31
What does Perceptual-Uniformity of A mean?
A=0.2
For all |A- A| = T() where T() is the median translucency difference between and perceived by the population
We need to adjust the parameters of A to minimize the error between predicted and perceived translucency difference
Note that it is unlikely that a perfect perceptually-uniform translucency space exists (curvature, diminishing returns phenomenon)
T=0.1
A=0.2
T=0.2
A=0.1

## Slide 32
For the reference materials:
We seek a psychometric function and a modified attenuation coefficient that embeds A into a perceptually-uniform scale, i.e. Euclidean distances agree with perceived differences
We need to know perceptual translucency differences  Psychophysical experiment
View Point
psychometric function
Assumption Stevens’ power law is applicable
modified attenuation coefficient
Assumption Scattering and absorption have different impact on perceived translucency
Perceptually-Uniform Embedding of A

## Slide 33
Psychophysical experiment
Use anchor pair of reference materials with a small but clearly visible translucency difference Tanchor
Determine for well distributed reference materials and directions the same difference by conducting a psychophysical experiment:
  Method of constant stimuli [Engeldrum 2000]
  Color-calibrated display
  Monte-carlo path tracer Mitsuba [Jakob 2010]
  40 subjects (6 female, 34 male)
Tanchor
Tanchor

## Slide 34
Psychophysical experiment
Use anchor pair of reference materials with a small but clearly visible translucency difference Tanchor
Determine for well distributed reference materials and directions the same difference by conducting a psychophysical experiment:
  Method of constant stimuli [Engeldrum 2000]
  Color-calibrated display
  Monte-carlo path tracer Mitsuba [Jakob 2010]
  40 subjects (6 female, 34 male)
Subjects were asked: Which pair has the larger perceived translucency? (left/right)
Test pair
Anchor pair

## Slide 35
Psychophysical experiment
Each experimentally determined pair t of reference materials correspond to a pair of A values with a difference of
Solve where is the set of pairs with the same perceived translucency difference as the anchor pair
Solution: (better uniformity than CIELAB)
Tanchor
Tanchor

## Slide 36
Perceptually-Uniform Embedding of A
Absorption and scattering coefficient in
parenthesis indicating the reference material

## Slide 37
Adjusting A to the print size

## Slide 38
Adjusting A to the Print Size
Problem: Perceived translucency depends on the size
Size X, Material A
Size Y, Material A
Size Y, Material B

## Slide 39
Adjusting A to the Print Size
air material B
Scaling an object does not change the mean scattering and absorption distances  The object appears more translucent
Scale absorption and scattering coefficients to preserve appearance
We can adjust to maintain the original translucent appearance of an object scaled by a factor
air material A

## Slide 40: Adjusting A to the Print Size
(a) and (b) have same A
A is adjusted in (c) to match (b)

## Slide 41
3D Printed Examples based on the A in RGBA Definition

## Slide 42: 3D Printed Examples
Revealing internal structures of complex models (28 sub-part). [skin: RGBA = (1,1,1,0)]
47 cm (polished)

## Slide 43: Translucency transitions
10 cm
Only a is altered.

## Slide 44: Translucency transitions
25 cm

## Slide 45: Control over translucent appearance
relative
relative
10 cm

## Slide 46: Reproducing translucent appearance
Real wax
3D Copy

## Slide 47: Increasing design space
Real wax
Appearance copy
Translucency copy
Same RGBA
Same shape + a

## Slide 48: Reproducing translucent appearance
violet stone
green stone
green soap
interpolate
interpolate

## Slide 49: Reproducing translucent appearance

## Slide 50: Summary
Proposed definition of A in RGBA for a joint color and translucency space is suitable for digital fabrication
  Low dimensional
  Encoding is supported by 3MF
  Encoding is supported by various design tools
  Device independent, which is necessary for an open system architecture
  Measurable with commercial reflectance/transmittance spectrophotometer
  Nearly perceptually uniform (better than CIELAB for color)
  Adjustable to print size for preserving translucency appearance at different scale

## Slide 51
Acknowledgements
Grants:
  AIF IGF-Vorhaben Nr. 18478 (Prozessstandardisierung im grafischen 3D-Druck für 3DP- und FDM-Verfahren)
  Scan4Reco project funded by EU Horizon 2020 Framework Programme under grant agreement no 665091
  Fraunhofer Attract 008-600075
Markus Barbieri (Spectro LFP CAD Design)

## Slide 52
Philipp Urban
Head of Competence Center 3D Printing Technology
Fraunhofer Institute for Computer Graphics Research IGD
Fraunhoferstraße 5
64283 Darmstadt
Tel +49 6151 155 –250 | Fax –480
Philipp.urban@igd.fraunhofer.de
www.igd.fraunhofer.de

## Slide 53
Backup Slides

## Slide 54
Meaningful Edge-Loss Measurements

## Slide 55
Meaningful Edge-Loss Measurements? (Detectability)
Each red dot indicates the edges-loss measurement for a PSF with
a decay of 50% at the corresponding cpd
All edge-loss difference measurements are larger than L* =1 and detectable by spectrophotometers used in graphic arts

## Slide 56
Meaningful Edge-Loss Measurements? (Discrimination)
Human and
Spectro
only
Spectro
Neither
Human nor
Spectro
Spectrohotometric distrimination threshold: 0.5 Based on medium term repeatability of 0.24 [Wyble and Rich 2007]
Human discrimination
Viewing distance 80cm
Convolute with CSF [iCAM framework, Fairchild and Johnson 2004]
Pixel-wise difference
Average over non-zero differences
Threshold L* =1

## Slide 57
Perceptually-Uniform Embedding of A

## Slide 58
Perceptually-Uniform Embedding of A
We conducted visual experiments using the method of constant stimuli on samples presented on a color calibrated display.
A virtual viewing booth was designed with defined viewing conditions
Rendering was performed by solving the spectral radiative transfer equation using the physically-based path-tracer Mitsuba

## Slide 59
Method of Constant Stimuli
Binary results were evaluated using probit analysis
T50 distances in scattering coefficient were determined T50 = Distance from a center sample at which 50% of the subjects perceived the anchor to be larger and 50% to be smaller
Perceptually-Uniform Embedding of A

## Slide 60
The parameters were optimized for the visual translucency differences by minimizing the perceptual disagreement resulting in:
We computed the Standardized REsidual Sum of Squares (STRESS) index to quantify the difference between measured and predicted perceived difference)
STRESS index dropped from 49.7 (no optimization) to 32.7 (approx. similar to CIE94 color difference formula in CIELAB)
Perceptually-Uniform Embedding of A